## Slide 1: One year review of the Emerging Technology Grant for Digital Systems Education
Jim Brakefield jim.brakefield@ieee.org
IEEE Computer Society
Notes: Tinker toy (or LEGO block) construction embodies the generation/design of abstract objects from simple uniform components

## Slide 2: Preliminaries
Funding provided by a grant from the IEEE Computer Society as part of their Emerging Technologies program
St. Mary’s University provided classrooms
I’m Jim Brakefield, jim.brakefield@ieee.org
Full set of files at: https://github.com/jimbrake/20-dollar-FPGA-kit
Introduction to FPGA video: https://www.youtube.com/watch?v=EVy4KEj9kZg

## Slide 3: Caveats
This is a search for lowest cost parts
Availability and pricing may vary
Ordering from AliExpress typically takes a month for delivery
In the last few years FPGA boards have dramatically increased in price + chip shortages
At the university level and for best experience there are boards for $80 (academic pricing)

## Slide 4: Outline
Some FPGA basics
The FPGA Boot Camp review
  Choice of boards
    Terasic DE-10 Lite
    RealDigital Boolean board
  Comments
The $20 FPGA kit choices
  The Seeed Studio Tang nano 9K
  The Alinx AX309 Spartan-6 board
Advanced FPGA subjects of note
  RealDigital board selection
  AMD/Xilinx academic boards
  Intel/Altera academic boards

## Slide 5: FPGA Basics
LUTs Four to six inputs, one or two outputs
  Consistent within a family of parts
  A 6LUT equals approximately 1.5 4LUTs
D flip-flops Clock & D in, Q & not-Q out
Block RAM Two R/W ports, aspect ratio adj.
IO pins Voltage & drive strength adj.
DSP Multiply and/or accumulate
Tools Open source or vendor provided
  Free tools for small & medium size low cost parts
Notes: IO pins, via constraint files, support dozens of IO standards. DSP multipliers vary from 16 by 16 to 18 by 25 with varying capabilities for cascading. Usually one DFF per 4LUT and two DFF per 6LUT.

## Slide 6: LUT + DFF Lattice Semiconductor iCE40FamilyHandbook.pdf pg6-2
Notes: Most FPGA families have the carry chain after the LUTs and before the DFF.

## Slide 7: LUTs
Performing Boolean Algebra inside an FPGA using Look-Up Tables (LUTs)
https://nandland.com/lesson-4-what-is-a-look-up-table-lut/:
“Note to the reader: many textbooks and classrooms will spend a
significant amount of time discussing how LUTs can be wired to
create the optimal solution to a Boolean expression. Optimal
means that it uses the least number of gates possible. Topics
such as De Morgan’s Law, Karnaugh Maps, the Quine-McCluskey
method, and others are usually discussed at great length that
describe how to optimize digital logic. However I feel that this is
not necessary to begin learning about FPGAs.”
Notes: The four main user visible components of an FPGA: LUTs, block RAM, D flip-flops and IO pins. DSP units include a multiplier and an accumulator. All connected by programmable wiring.

## Slide 8: Block RAM tutorial
https://nandland.com/lesson-15-what-is-a-block-ram-bram/
A full dual port block RAM has two sets of address, read data and write data along with clock and byte write enables.
Notes: The four main user visible components of an FPGA: LUTs, block RAM, D flip-flops and IO pins. The others include clock generators and the DSP/multiply/accumulator.

## Slide 9: Simplified DSP48A1 slice Xilinx Spartan-6 FPGA DSP48A1 Slice pg 17
Notes: 18-bit by 18-bit two’s complement signed multiplier, 48-bit accumulator.

## Slide 10: The FPGA Boot Camp task
Establish a minimum set of features
Find lowest cost boards
Establish a Boot Camp program/slide deck
Modify the Digital Designer tool
Conduct the classes
Comments
  Modest price increases
  Vivado disk space
  Local university courses
Notes: Trinity and St. Marys use Terasic DE-10. UTSA uses BASYS-3 ARTIX-7. Boards signed out to the student for the semester.
Terasic DE-10 Lite went from $77 to $82 (academic prices). Realdigital.org Boolean board went from $69 to $74 (academic prices).

## Slide 11: The FPGA Boot Camp Board choices
Realdigital.org Boolean board
  Located in USA
  15 week courseware
  (16) switches & LEDs, (8) 7-segment digits
  Constraint files generated by Digital Designer
Terasic DE-10 Lite
  Located in Taiwan
  Some course material https://fpgacademy.org/courses.html
  (10) switches & LEDs, (6) 7-segment digits
  Academic pricing harder to obtain
Notes: Shipping from Realdigital.org was from three to five days. Boot Camp files at https://github.com/jimbrake/FPGA_Boot_Camp have a date code suffix and are updated occasionally.

## Slide 12: DE10-Lite versus Boolean board
  DE10-Lite Boolean board
  50K 4LUT MAX-X = 33K 6LUT Spartan-7
  1.7Mb block RAM = 2.8Mb block RAM
  64MB DRAM + No DRAM
  SD card slot + No SD card slot
  VGA = HDMI
  Quartus 15GB + Vivado 33GB (no Vitis)
  Schematic capture = Use Digital Designer
  Use constraint editor ++ Generated constraint file
  $82 + $74
  Ready to use = Ready to use
  Mainstream tools (Quartus) = Mainstream tools (Vivado)
  Usable without wiring = Usable without wiring
  Slide switches = Slide switches
Notes: The user requirements (switches, push buttons, LEDs and 7-segment digits) narrowed the choices down to these two boards. A major (self study) factor was the availability of a 15 week courseware for Boolean board at RealDigital.org. Currently several universities issue an FPGA board to each student for a one semester course.

## Slide 13: The FPGA Boot Camp agenda With plenty of hands-on (lab) time
Two Saturdays with lunch from Jason’s, 9AM-4PM
First Saturday:
  Introductory FPGA video (20 minutes)
  Install Digital Designer
  Configure for Boolean Board
  Students draw schematic(s) & exercise schematic
Second Saturday:
  Examine generated VHDL/Verilog & constraint file
  Install Vivado
  Show Vivado project creation & flow
  The students install circuit created on previous Saturday
Notes: Many thanks to St. Mary’s University for providing the classrooms.

## Slide 14: The FPGA Boot Camp Comments
Students
  from 9th grade to grad students & continuing ed.
  High school: mostly from STEM & charter school
Vivado needed 80GB of disk space!
  Horrors, later trimmed to 33GB (don’t install Vitis)
Students given their boards on 2nd Saturday
High number of no-shows
Intel/Altera tool (Quartus) supports schematic capture with manual entry of constraints

## Slide 15: The $20 FPGA Kit agenda
To make the FPGA experience available to all
Very few FPGA boards for under $20
The complete Tang 9K Nano kit $18 in quantity
  DRAM, SD card slot, HDMI & LCD connectors
  Use add-on 7-sgement display with buttons, LEDs
The Alinx Spartan-6 $31 with JTAG programmer.
  DRAM, SD card slot, VGA connector
  Has 7-segment display, buttons & LEDs
Both have ~9K LUTs, Block RAM & DSP units
Unable to find an comparable Intel/Altera board
Notes: The LUT count, DRAM and SD card slot means that the board can be used for soft core processors such as 6502, Z80, AVR etc. The SD card can be used as a disk file device supporting an operating system. https://www.cnx-software.com/2022/01/17/tang-nano-9k-fpga-board-can-emulate-picorv32-risc-v-soft-core-with-all-peripherals/

## Slide 16: Tang Nano 9K kit assembled
The kit using the Tang 9K Nano for high volume has a per kit price of $17.89
In low volume (for a single kit) is $25.93 plus shipping and taxes with some
spare parts left over (extra breadboards and jumper wires).
Notes: Pricing for thirty kits for a classroom about $20 each plus shipping and taxes. Spreadsheet has several sources for each of the items. One could use two five position DIP switches? Be sure to get jumpers with insulated ends. For a long breadboard picture see Long Breadboard slide. The longer breadboards have power rows aligned with pin columns.

## Slide 17: Alinx Spartan-6 board & JTAG
The Alinx Spartan-6 requires a JTAG programmer, shown attached
Notes: Kit price quantity one: $31.20, by sharing a JTAG programmer: $20.77 plus taxes & shipping. Uses Xilinx mature ISE tools. JTAG programmer shown has full set of cables (recommended).

## Slide 18: The Alinx Spartan-6 kit
Full set of buttons, LEDs & 7-segment digits
Supplement the Spartan-6 board:
  JTAG programmer $11.30 for one
    Price varies widely from $11 to $200+
  Shorting jumpers $0.85 for ten
    A substitute for slide switches
And learning the Xilinx ISE software tools
  ISE not recommended for new students
  Can make an exception for high school students
  ISE 14.7 takes 17GB installed
https://github.com/alinxalinx/AX309 documentation
Notes: The Digital simulator can be used to generate the VHDL or Verilog (https://github.com/hneemann/Digital/). ISE does not require constraint files.

## Slide 19: The Tang nano 9K kit
Supplement the Tang 9K Nano FPGA board:
  Display board: $2.90
  12 position DIP switch $1.06 for one
  Solderless bread board $6.69 for four
Will require some user wiring
  Insulated 22 gauge jumper wire
  Five or more male-female jumper wires
  or replacing display board pins with jumper wires
  Pins on Tang FPGA board require soldering
And learning the Nano board software tools
  VHDL, Verilog and constraint files supported.
Notes: The Digital simulator can be used to generate the VHDL or Verilog (https://github.com/hneemann/Digital/). However, the constraint file needs to be edited or entered via Gowin constraint editor.

## Slide 20: Display board tm1638-7-segment-display-keypad-led-module
Provides:
8 7-seg digits
8 discrete LEDs
8 push buttons
for $2.90
Notes: Uses 4 volt driver chip, should work at 3.3 volts? Driver chip uses a SPI like interface. VHDL/Verilog example web links on sheet titled “RTL for driving display”.

## Slide 21: DIP Switch
For use on breadboard will need to fold out every 6th pin.
Twelve position DIP switch gives best cost/ benefit ratio.
Notes: Individual slide switches are relatively expensive. For best connections to breadboard use DIP switches with full size pins (shown). To reclaim folded out pins solder a fine wire up and down the fold-out side (the side normally connected to ground).

## Slide 22: Solderless Breadboard
Best deal in quantity three
or sixteen
The DIP switch
to straddle
ground column
and signal rows
Sufficient size to hold Tang Nano and DIP switch
Notes: As the ground column has breaks every six spaces, will fold the DIP switch pins out for those positions; or use two five position DIP switches.
Longer versions of the breadboard available or double this module for more prototype space.

## Slide 23
Tang 9K Nano
approximately $13 + shipping
2/21/2023
23
Notes: Uses Gowin GW1NR-9 FPGA: 8,640 LUTs, 2 push buttons, 6 LEDs, HDMI connector, SD slot, DRAM, Two LCD connectors.
Usually has unsoldered pins. User to solder the pins needed for breadboard use. Many other low cost DIP format FPGA boards available, just not as capable for the price.

## Slide 24: RTL for driving display
VHDL and Verilog for operating the TM1638 display board available at:
https://github.com/zpekic/Sys_TM1638
https://github.com/alangarf/tm1638-verilog
Notes: Both flat cable connectors & HDMI connector accessible. Breadboard scored with knife and split allowing access to more breadboard rows. Top power buss rotated 180 degrees and shifted to align with DIP switch pins. Adhesive breadboard backing exposed and mounted on piece of wood. Rubber bands used to hold display board & dress the jumpers.

## Slide 25: Tang nano 9K: What is missing
Tutorials:
  https://learn.lushaylabs.com/tang-nano-series/
  https://wiki.sipeed.com/hardware/en/tang/Tang-Nano-9K/Nano-9K.html
Courseware for the middle school student
  Not planning to produce it
  Not my area of expertise
Goal is for the middle school student to get familiar with digital circuits and binary
  Preprogram so IO pins provide logic gate inputs to Tang nano board circuits (gates), gate outputs drive LEDs
  Better yet, make use of Display board in a similar fashion
Notes: By preprogramming the board, students can get “instant gratification” on using logic gates, buttons and LEDs. Using the display board comes later, again for instant gratification preprogram an example operation using the display board. Need to adapt Digital Designer for nano 9K and Spartan-6 boards.

## Slide 26: $20 kits versus full feature board
  Tang nano 9K Boolean board
  $20 versus $74
  Some user wiring & soldering Ready to use
  Buggy FPGA tools Mainstream tools
  Needs case for transport Usable without wiring
  DIP switches Slide switches
  Alinx Spartan-6 Boolean board
  $25 versus $74
  Ready to use Ready to use
  Dated tools Mainstream tools
  Need to connect JTAG Built-in JTAG
  Shorting jumpers Slide switches
Notes: Files at https://github.com/jimbrake/FPGA_Boot_Camp have a date code suffix and are updated frequently. Currently several universities issue an FPGA board to each student for a one semester course. Am targeting middle school students (and the third world) with this kit,

## Slide 27: Digital-Designer logic simulator
Web site: https://github.com/hneemann/Digital/
Authored by: Helmut.Neemann@mosbach.dhbw.de
Open source, other simulators available
Modified to support the Boolean board
Here, the user can use Digital for simulation
  And examine the generated VHDL/Verilog
  Usually without errors, great for the beginner!
Notes: You will probably need to manually generate constraint files for Tang 9K Nano or use the Gowin constraint editor (recommended).

## Slide 28: Interactive digital simulation
Schematic editor and simulator
Provides an intermediate step before RTL (Register Transfer Logic) and full FPGA tools.
Requires nothing beyond a PC.
Requires Java
Totally interactive
Generates VHDL or Verilog RTL files
Generates constraint file for vivado (the xilinx FPGA tool)
Notes: The two main RTLs are verilog and VHDL. The most recent verilog is called System Verilog. ASIC people prefer verilog. DOD and Europe like VHDL. There are linting tools that can check your code including adherence to coding standards.

## Slide 29
2/21/2023
29
FPGA board rankings
Top version sorted by LUT count, bottom version by block RAM bit count
This listing is only a sample of the hundreds of boards available.
2/21/2023
29

## Slide 30: RTL (Register Transfer Language) VHDL and Verilog are “hardware description” languages
Separates design into combinatorial (logic) and sequential (registers).
For simple designs use a single clock
  Tang Nano 9K clock is 27 MHz
  Digital will generate slower clocks
    Right click on clock icon & set frequency
    Digital thinks the clock is 100MHz
Registers update on rising edge clock
Notes: This FPGA Boot Camp avoids teaching VHDL or Verilog, instead you learn by seeing the VHDL or Verilog generated from your schematic. This is done to get to an easy to use FPGA “flow” (a sequence of actions needed to create and implement a design).

## Slide 31: Side by side VHDL and Verilog
Digital generates both
RealDigital’s treatment:
  https://www.realdigital.org/downloads/e06bddc63669cbc91ae981df18bcf3c5.pdf
Side by side System-Verilog & VHDL:
  Digital Design and Computer Architecture, Harris & Harris, 2nd ed. Also ARM and RISC-V editions
  Highly recommended, goes from transistors to PCs
Side by side Verilog & VHDL:
  HDL Programming Fundamentals: VHDL and Verilog, Nazeih Botros 2006
Also: https://www.fpga4student.com/2017/08/verilog-vs-vhdl-explain-by-example.html
Notes: System Verilog is a modern version of Verilog and provides the same capabilities as VHDL.

## Slide 32: What FPGA tools do
Much goes on behind the scenes
Circuit is optimized (logic simplification)
  unused stuff is pruned, if no outputs then all pruned
Circuit is mapped into FPGA primitives
Circuit wired up with FPGA routing resources
Bit file generated that configures the chip
Error checking especially missing semicolons
Reports on timing, resources used, error messages
A schematic viewer will show chip details
Elaborated Design show’s vivado’s version of schematic
Notes: FPGA tools are very good at logic optimization and good at interconnecting logic units, not perfect on placement of LUTs and Block RAMs.
Tools allow optimization for speed and area with level of effort controls. Often times optimization for area also gives good speed.
Modern practice is to use a constraint file to set the desired clock speed and let the FPGA tool optimize for that setting.

## Slide 33
My view of binary
Zero and ones: One names a single such signal or a group of such signals (subscripted by bit number)
A binary number is a polynomial:
  A[n-1]xn-1 + A[n-2]xn-2 + … A[1]x1 + A[0]x0
  Where X = 2, and A[n] are 0 or 1 bits from the number. If A[n-1] is 0/-1 then it is 2’s complement and negative if A[n-1] is -1.
  It is typical for the bit numbers to run from N-1 to 0 where N is the number of bits.
  Adding or subtracting 2’s complement wraps around in a circle where the most positive and most negative numbers are adjacent (any carry or borrow beyond xn-1 is discarded).
Windows calculator has binary features: https://www.youtube.com/watch?v=PK5WQqN3_44
Max Maxfield’s explanation of binary:
https://www.eejournal.com/article/mysteries-of-the-ancients-binary-coded-decimal-bcd/
Notes: The youtube video covers all the calculator features including radix (binary, hex, decimal) and the binary operations (AND, OR, XOR, shifts and rotate). Maxfield explains more than just BCD and binary.

## Slide 34: FPGA Video Tutorials
There are a wealth of youtube videos on these subjects including whole sets of videos
https://nandland.com/fpga-101/ and
https://www.youtube.com/watch?v=CfmlsDW3Z4c
https://www.youtube.com/watch?v=OUNrGLgx9h4
  Recommended
My favorite FPGA video series:
  https://www.youtube.com/@SimplyEmbedded/videos
  https://www.youtube.com/@SimplyEmbedded/playlists

## Slide 35: Advanced FPGA boards and education
A continuum of boards from basic to very advanced
  Large FPGAs: millions of LUTs, GHz serial IO
Corresponding tutorials and videos:
  Advanced applications: vision, neural nets, high speed A2D and D2A, robotics, etc.
Research on making FPGAs easier to use:
  HLS (High Level Synthesis) generating VHDL/Verilog from C/C++
  Providing means to handle the time/space trade-offs
    VAST laboratory UCLA, Jason Cong
Notes: https://digilent.com/blog/teaching-computer-architecture-with-fpga-boards-harris-harris/. VAST laboratory UCLA, Jason Cong: https://vast.cs.ucla.edu/publications

## Slide 36: Intel/Altera academic program
https://www.intel.com/content/www/us/en/developer/topic-technology/fpga-academic/overview.html
https://www.intel.com/content/www/us/en/developer/topic-technology/fpga-academic/materials.html
https://fpgacademy.org/tools.html
  https://fpgacademy.org/courses.html
DE10-Lite academic price $82
Notes: Only two push buttons. Least expensive Altera board with “full” user IO. VGA video output, DRAM chip & microSD card slot. Arduino connectors.

## Slide 37: RealDigital boards
Notes: About half way through 2022 RealDigital.org added the bottom row of parts.

## Slide 38: Xilinx university program
https://www.xilinx.com/support/university.html
$74 $123 $200
$549
$2149
$7695
Notes: Boolean Board “endorsement” by Xilinx. Kria-KV260 has state-of-the-art FPGA.

## Slide 39: Xilinx basic academic boards
Notes: https://www.xilinx.com/support/university/xup-boards.html. The FPGA part numbers for two leftmost boards are swapped.

## Slide 40: Xilinx academic boards w/ARM uPs
Notes: https://www.xilinx.com/support/university/xup-boards.html

## Slide 41: Xilinx high end academic boards
Notes: https://www.xilinx.com/support/university/xup-boards.html. The Kria SOM has only a single PMOD for user IO. Does have RJ45, HDMI & camera connectors.
The “See more details” buttons will show the use cases.

## Slide 42: Intel/Altera education program https://fpgacademy.org/boards.html
A very high end board, the others also from Terasic
Notes: The more advanced boards in the research boards section.

## Slide 43: Tang 9K using long breadboard
Tang nano 9K mounted on full length breadboard
9K rotated 180 degrees for access to HDMI connector
Barely able to connect USB
Not enough rows for good access to IO pins
Notes: Plan to cut the breadboard in half, split in two and mount two pieces on wood like the short breadboard picture.

## Slide 44: Long breadboard picture
Cmod A7-15 board from Digilent, DIP switch and TM1638 display board
Pin 6 of DIP switch folded out and not connected
Male-female jumper wires used to connect the display board
Solid wire jumper connects one side of DIP switch to ground
Notes: Using parts on hand. Cmod A7-15T: https://www.tequipment.net/Digilent/Cmod-A7-15T/. In above picture the jumper ends are not insulated, use ones with insulated ends.

## Slide 45: Boolean board $74
Notes: https://www.realdigital.org/ Uses AMD/xilinx tools(vivado). HDMI video out. Available with or without Bluetooth LE. 35K 6LUTs. Four Pmods.

## Slide 46: mess of wires not cool any more
From https://life.ieee.org/
In today’s world
most wires are
in the PCB and
In the FPGA !
OK as long as you
don’t need to
move the device
Notes: For more organized and stable proto-board wiring see a Ben Eater's web page: https://www.reddit.com/r/beneater/comments/w447u3/created_a_random_maze_program_for_my_putey1_ttl/

## Slide 47: Educational programs
Intel/Altera academy Quartus: RTL & Schematic
AMD/Xilinx university program ISE & Vivado RTL tools
Courseware for Real Digital Boolean board (RTL)
  https://www.realdigital.org/course/digital-logic-for-the-boolean-board
https://www.tina.com/ (Schematic based, not free)
  Support for the Digilent Basys 3 and the Terasic DE10-Lite FPGA boards
  https://www.tina.com/blog/programming-fpga-boards-with-tina-using-schematic-design-entry/
Digital logic simulator (Schematic based)
    Support for the Digilent Basys 3 and the TinyFPGA-BX boards
  https://github.com/hneemann/Digital/
Hundreds of youtube videos and tutorials on the internet
ARM has an education kit using an FPGA
Notes: RTL: Register transfer language, usually VHDL or Verilog. Quartus and Vivado are mainstream tools with free education variants (reduced FPGA family support). Xilinx ISE not recommended for new users. ARM has courseware for their soft-core ARM on an FPGA: https://github.com/arm-university/Advanced-System-on-Chip-Design-Education-Kit

## Slide 48: FPGA References
Twelve youtube videos on specific FPGA features (uses verilog RTL): https://www.youtube.com/playlist?list=PLEBQazB0HUyT1WmMONxRZn9NmQ_9CIKhb
Three Ages of FPGAs: A Retrospective…, Steve Trimberger, Proc. IEEE v103#3p318, 2015
  www.cpe.virginia.edu/grads/pdfs/January%202016/VLSI.pdf
  https://www.youtube.com/watch?v=4ntXSyOhlBY
  Xilinx Part Family History, John Lazzaro,
  www-inst.eecs.berkeley.edu/~cs294-59/fa10/resources/Xilinx-history/Xilinx-history.html
Altera History, corporate, http://www.fundinguniverse.com/company-histories/altera-corporation-history/
Low cost FPGA boards
  https://www.joelw.id.au/FPGA/CheapFPGADevelopmentBoards
Open source IP https://opencores.org/projects
Github (open source) projects: search on “github vhdl verilog cpu”
Notes: http://www.fundinguniverse.com/company-histories has histories of Xilinx and many other companies.